# SECTION 07 32 31 SYNTHETIC ROOF TILES

This section includes editing notes to assist the user in editing the section to suit project requirements. These notes are included as hidden text, and can be revealed or hidden by the following method in Microsoft Word:

Display the FILE tab on the ribbon, click OPTIONS, then DISPLAY. Select or deselect HIDDEN TEXT.

This guide specification section has been prepared by DaVinci Roofscapes, LLC for use in the preparation of a project specification section covering synthetic roof tiles for use as steep slope roofing.

The following should be noted in using this specification:

Hypertext links to specific websites are included after manufacturer names and names of organizations whose standards are referenced within the text, to assist in product selection and further research.

Hypertext links are contained in parenthesis and shown in blue, e.g.:

(www.astm.org)

Items requiring user input are enclosed within brackets and included as red text, e.g.: Section [09 00 00] [ 	.]

Optional paragraphs are separated by an "OR" statement included as red text, e.g.:

**** OR ****

Sustainable requirements are included for projects requiring LEED certification, and are included as green text. For additional information on LEED, visit the U.S. Green Building Council website at www.usgbc.org.

For assistance on the use of the products in this section, contact DaVinci Roofscapes, LLC by calling 800- DAVINCI, by email at mstone@davinciroofscapoes.com, or visit their website at www.davinciroofscapes.com.

# PART 1	GENERAL

  - SUMMARY

Edit the following to include only those items specified in this section.

    - Section Includes:

      - Synthetic roof tiles, underlayment, flashings, fasteners, and accessories.

Coordinate the following with other sections in the Project Manual.

    - Related Requirements:

      - Division 01 - General Requirements: Administrative, procedural, and temporary work requirements.

      - Section [07 62 00 - Sheet Metal Flashing and Trim.] [ 	- 	.]

      - Section [07 92 00 - Joint Sealers.] [ 	- 	.]

  - REFERENCES

Edit the following to include only those references used elsewhere in this section.

    - American Society for Testing and Materials (ASTM) (www.astm.org):

      - D226/D226M - Standard Specification for Asphalt-Saturated Organic Felt Used in Roofing and Waterproofing.

      - D3161/D3161M - Standard Test Method for Wind-Resistance of Asphalt Shingles (Fan-Induced Method).

      - E108 - Standard Test Methods for Fire Tests of Roof Coverings.

    - California Department of Forestry and Fire Prevention (Cal-Fire) (www.fire.ca.gov) - Listing Service.

    - National Research Council Canada, Canadian Construction Materials Centre (CCMC) (www.nrc-cnrc.gc.ca) - Evaluation Report 14094-R.

    - Underwriters Laboratories (UL) (www.ul.com):

      - 790 - Standard for Standard Test Methods for Fire Tests of Roof Coverings.

      - 2218 - Standard for Impact Resistance of Prepared Roof Covering Materials.

  - ADMINISTRATIVE REQUIREMENTS

Retain the following for a pre-installation conference to review the work of this section prior to installation.

    - Pre-Installation Conference:

      - Convene at Project site [2] [ ] weeks prior to beginning work of this Section.

      - Attendance: [Architect,] [Contractor,] [Construction Manager,] installer, and related trades.

      - Review and discuss:

        - Installation procedures and manufacturer's recommendations.

        - Safety procedures.

        - Coordination with installation of other work.

        - Availability of materials.

        - Preparation and approval of substrate and penetrations through roof.

        - Other items related to successful execution of work.

  - SUBMITTALS

Retain the following for submittals requiring the Design Professional’s review.

    - Action Submittals:

      - Shop Drawings: Show tile layout, method of attachment, flashings, trim, conditions at eaves, intersections with adjacent materials, and other installation details.

      - Product Data: Manufacturer's data sheets on each product including:

        - Tiles, underlayment, flashings, fasteners, and accessories:

          - Indicate composition, properties, and dimensions.

          - Show compliance with specified requirements.

        - Preparation instructions and recommendations.

        - Storage and handling requirements and recommendations.

        - Installation methods.

      - Samples:

        - Selection Samples: Two sets of color chips representing manufacturer's full range of available colors and surface textures.

        - Verification Samples: After selection, submit two samples representing actual product, color, and texture.

Retain the following for projects requiring sustainable documentation.

    - Sustainable Design Submittals: Refer to Division 01.

Retain the following for extra materials for the Owner's maintenance after completion.

    - Maintenance Material Submittals: Provide [ ] square feet of extra tiles.

  - QUALITY ASSURANCE

Retain the following if required; edit to suit project requirements.

    - Manufacturer Qualifications: Company specializing in manufacture of synthetic tiles.

    - Installer Qualifications: Minimum [3] [ ] years experience in work of this Section.

Retain the following for field or shop mockups for review of construction, coordination of work of multiple sections, testing, or observation of operation.

    - Mockup:

      - Provide mockup of tiles, underlayment, and related flashings.

      - Size: Minimum [8 x 8] [ 	x ] feet.

      - Locate [where directed.] [ 	.]

      - Approved mockup [may] [may not] remain as part of the Work.

  - DELIVERY, STORAGE AND HANDLING

    - Ship tiles in bundles:

      - Collate in sequence of widths and colors as required for selected color blend.

      - Assemble bundles so that sorting at job site is not required.

    - Deliver tiles to site in manufacturer's unopened, labeled bundles.

      - Verify quantities and condition upon delivery.

      - Remove damaged products from site.

    - Store products in protected environment, off ground, protected moisture, traffic, and construction activities.

    - Store tiles flat. Do not store on site for prolonged period.

    - Store products at temperature between 40 and 120 degrees F (4 degrees C and 49 degrees C).

    - Store and dispose of solvent-based materials, and materials used with solvent-based materials, in accordance with requirements of authorities having jurisdiction.

  - SITE CONDITIONS

    - Environmental Requirements:

      - Observe manufacturer’s temperature, humidity, and moisture limits.

      - Do not install products under environmental conditions outside manufacturer's absolute limits.

  - WARRANTIES

    - Furnish manufacturer’s 50 years warranty against breakage and deterioration resulting in leaks under normal weather and use conditions.

    - Furnish installer's 2 years total roof system warranty against water penetration, including underlayment, flashings, trim, and other roof components.

# PART 2	PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: DaVinci Roofscapes, LLC, 800-DAVINCI, www.davinciroofscapes.com.

Edit the following to indicate whether or not substitutions will be permitted for the products in this section.

    - Substitutions: [Refer to Division 01.] [Not permitted.]

  - MATERIALS

    - Performance Requirements:

      - Roof system: Manufactured synthetic tiles attached to structural substrate to form weather tight roof envelope with no measurable water penetration.

      - Method of attachments designed to adequately resist wind uplift for roof configuration and Project location.

      - Meet minimum uplift resistance of [93] [186] PSF with 2:1 safety factor in accordance with TAS 125.

Retain the following for Province Slate tiles.

    - Synthetic Slate Tiles:

      - Description: Lightweight, synthetic roof tiles with appearance, color, texture, and thickness of natural quarried slate shingles.

      - Product: Province Slate.

      - Material: Engineered polymer formulated from 100 percent virgin plastic resins; recycled materials not acceptable.

      - Performance characteristics:

        - Fire resistance Class A installed over one layer of Eco Chief Solarhide™

        - Fire resistance Class C installed over minimum 30lb felt that meets ASTM 226 Type II standard

        - Impact rating: Class 4, tested to UL 2218.

        - Wind rating: 110 MPH, tested to ASTM D3161

        - Hurricane zone force wind rating: 180 MPH, tested to TAS 125.

        - Approved by NRCC CCMC.

      - Size:

        - Width: 12 inches (305 mm).

        - Length: 11-1/2 inch (397 mm).

        - Thickness: 1/2 inch (13 mm) at butt, 3/8 inch (9.5 mm) at top.

      - Starter shingle: 3.5 inches (89 mm) long x 11.5 inches (292 mm) wide.

      - Markings: Form shingles with markings on upper surface to indicate nailing locations and provide alignment guidelines.

      - Color:

        - Provide shingles in color comparable to natural slate.

        - Provide internal ultraviolet stabilizers.

Contact DaVinci Roofscapes, LLC for information about special orders.

      - Color:

        - Provide shingles factory blended in multiple colors.

        - Blend: [Brownstone]  [Castle Gray] [European] [Smokey Grey] [Slate Black] [Slate Gray] [Custom.]